## Slide 1: MMS236 DT1 Presentation
Connecting humanity again – environmentally friendly this time!

## Slide 2: Hand-drawing concept
Turboprop – the perfect engine for the job
Top wing - allowing for a bigger propeller
Wing root tanks – an eagle needs its shoulders

## Slide 3: Sizing mission
Take-off – 1400m airstrip
Cruise – 1100 nm @ Mach 0.5
Descent – 199 knots approach speed
Land – 1350m airstrip
Loiter - 20 min (200 knots @ 1500 ft)
Diversion - 100 nm
Reserve – Contingency and trapped fuel, 6%

## Slide 4: Technology Assumptions – Engine performance
SFC = 11.4 mg/Ns
Tried to do a dimensional analysis to get for hydrogen, but to no avail

## Slide 5: Technology Assumptions - Aerodynamics
Aspect ratio = 12
Swet/Sref = 6.1
L/D_max = 16.8
L/D_cruise = 16.8
L/D_loiter = 14.6
Based on the ATR 72 Turboprop family

## Slide 6: Technology Assumptions - Weight
= 0.585
Assumed a 4% improvement of due to technological achievements
Assumed a 12% worsening of due to hydrogen tanks being heavy in themselves

## Slide 7: Selected concept
= 36.1 tonnes
= 5 tonnes
Tank volume = 70.4
“If I have seen further, it is by standing on the shoulders of giants.”